## Slide 1: Microprogram sequencing
by
Prof. Upendra Mishra
KIET Group of Institutions, Delhi-NCR, Ghaziabad

## Slide 2: Micro-programmed Control organization
A control memory is assumed to be a ROM, within which all control information is permanently stored.
The control address register (CAR) specifies the address of the micro-instruction and control data register holds the micro-instruction read from the memory.
A microinstruction contains a control word that specifies one or more micro-operations for the processor. Once these operations are executed, the control must determine the next address.
The location of the next micro-instruction may be the one next in the sequence or it may be located somewhere else in the control memory.
The next address generator is sometimes called a micro-program sequencer as it determines the address sequence that is read from memory.

## Slide 4: Micro-programmed Control Unit
The basic components of a microprogrammed control unit are:
    The control memory
    The circuits that select the next address called microprogram sequencer

## Slide 5: Microprogram Sequencer
The next address generator is sometimes called a microprogram sequencer, as it determines the address sequence that is read from control memory.
The purpose of a microprogram sequencer is to present an address to the control memory so that a microinstruction may be read and executed. The next-address logic of sequencer determines the specific source to be loaded into the control address register (CAR).
The choice of address source is guided by the next-address information bits that the sequencer receives from the present microinstruction.

## Slide 6: Microprogram Sequencer
Typical functions of a microprogram sequencer are:
Incrementing the Control Address Register (CAR) by one
Loading an address from the control memory into the Control Address Register (CAR)
Transferring an external address
Loading an initial address to start the control operations

## Slide 7: Methods for generating Address
Increment the Control Address Register.
Unconditional/Conditional Branch depending on status bit flags.
Subroutine Call & return.
Mapping from machine instruction to microinstruction Address.

## Slide 8: Mapping From Machine Instruction to Microinstruction

## Slide 9: Micro-Instruction Format

## Slide 10: Block Diagram of Microprogram Sequencer
Components of Microprogram Sequencer:
MUX1
MUX2
Input Logic
CAR
SBR

## Slide 11: Multiplexer1: (MUX1)
The first multiplexer selects address from one of the following four sources and routes it into CAR.
Incremented
External
from microinstruction
SBR (SubRoutine Register)
S1 | S0 | Selection
0 | 0 | CARCAR+1
0 | 1 | CARAD
1 | 0 | CARSBR (return from Subroutine)
1 | 1 | CAR(2-5)DR(11-14), CAR(0,1,6)0

## Slide 12: Multiplexer 2: (MUX2)
The second multiplexer tests the value of a selected status bit
and the result of test is applied to input logic.
CD field of microinstruction selects one of the status bit in the second multiplexer.
CD | Condition | Symbol | 
00 | Always = 1 | U | Unconditional branch
01 | DR(15) | I | Indirect address bit
10 | AC(15) | S | Sign bit of AC
11 | AC=0 | Z | Zero value in AC

## Slide 13: Input Logic Design:
The input logic block has three inputs I0, I1 and T,
and three outputs S0, S1, and L.
Variable S0 and S1 select one of the source addresses for CAR.
Variable L enables the load input in SBR.
Input Logic equations:
S1= I1
S0= I1.I0+I1’ T
L= I1’I0T

## Slide 15: The truth table for input logic is given below:
BR Field |  |  | Input |  |  | MUX1 |  | Load SBR | Function
 |  |  | I1 | I0 | T | S1 | S0 | L | 
0 | 0 | JMP | 0 | 0 | 0 | 0 | 0 | 0 | CARCAR+1
0 | 0 | JMP | 0 | 0 | 1 | 0 | 1 | 0 | CARAD
0 | 1 | CALL | 0 | 1 | 0 | 0 | 0 | 0 | CARCAR+1
0 | 1 | CALL | 0 | 1 | 1 | 0 | 1 | 1 | CARAD, SBRCAR+1
1 | 0 | RET | 1 | 0 | X | 1 | 0 | 0 | CARSBR (return from Subroutine)
1 | 1 | MAP | 1 | 1 | x | 1 | 1 | 0 | CAR(2-5)DR(11-14), CAR(0,1,6)0

## Slide 16: References
COMPUTER ORGANIZATION AND ARCHITECTURE-DESIGNING FOR PERFORMANCE, EIGHTH EDITION by William Stallings
COMPUTER SYSTEM ARCHITECTURE- THIRD EDITION BY M. Morris Mano

## Slide 17: Thank You